## Slide 1: Efficient Semi-dynamic Composite Event Monitoring
Steven Lai

## Slide 2: Basic Idea - Issues
It costs energy when monitoring the events so try to save as much as energy as possible
Events must be monitored in a timely fashion
Issues for energy saving:
  Reduce total energy consumption
  Reduce hot-spot energy consumption (load balancing)

## Slide 3: Solutions Overview
Ideas:
  Reduce unnecessary monitoring while keep
  Balance between energy consumption and delay
Reduce total energy cost:
  Event cancellation / triggering
  Optimize wake-up time and frequency
Reduce hot-spot energy consumption
  Choose a different event detector each time

## Slide 4: Event Model
Event: a set of tuples containing (type, name, value)
Event area: the geographical area of the event.
Event rate: the rate that the event must be monitored. Each event may have a different rate.

## Slide 5: Subscription Model
Subscription: constraints on the attributes of the events
Subscription representation:
  cp1: f1(ea1, (eb1)) f2(ea2, (eb2)) … fn(ean, (ebm))
  cp2: f1(ea1, (eb1)) f2(ea2, (eb2)) … fn(ean, (ebm))
  …
  cpn: f1(ea1, (eb1)) f2(ea2, (eb2)) … fn(ean, (ebm))
Each fn is a function on certain attributes with returning value of either true or false:
  f attr(en, em) = en.attr – em.attr op c
  fattr(en) = en.attr op c

## Slide 6: Subscription Model
Primitive Event:
  en: f1(en) f2(en) … fm(en)
Composite Event:
  We can find a row in all the event filters such that in this row ‘ec: f1(e1, e2) f2(e3, e4) … fn(em-1, em)’ where there exists ec!=en (en ∈ { e1, e2 … em})

## Slide 7: Network Model
Sensors are randomly deployed in an area.
One sink
All nodes are static
Mathematical representation: G=(V, E)

## Slide 8: Event Monitoring
Event Detection: bottom-up
Cost Estimation for Event Monitoring: top-down

## Slide 9: Event Detection – Primitive Events
Collect the results from the sensors.
Issues:
  High energy cost if need to collect results for every round for every event
  Sometimes not necessary to always collect results from the sensors
Solution to the Issues:
  Determine the cost and gain for each detection
  Put the sensor to sleep if cost > gain

## Slide 10: Event Detection
Start from primitive events.
Cost estimation for detecting composite events.
Cost estimation for a single event e is determined by the geographical area of the event: ce=fgeo(e)

## Slide 11: Cost Estimation Model

## Slide 12: Cost Estimation Algorithm
Given:
  A set of events E
  A set of event filters F
  The probability of the occurrence of each primitive event e in E: P={p1, p2, … pn}
Estimate the minimum cost to monitor an event ei in E

## Slide 13: Cost Estimation Algorithm
Find the sub-tree which has a root of ei
From the leaves of the trees, recursively determine the cost of each event by looking at its filters.
The following 2 rules are used:
  If the filter is ‘f(e)’: cf=ce
  If the filter is ‘f(e1, e2)’: cf=ce1+ce2+c1,2
Among all the filters f for event ei, the minimum one is the cost to monitor ei

## Slide 14: Event Monitoring Algorithm
For each fi in F, use the cost monitoring to determine the cost of fi.
If two events are used to compose another event, then the nodes need to make a decision on whether both need to be detected.
Once the cost is decided, the event will monitor the events from the least cost filter.

## Slide 15: Pseudo Codes for Cost Estimation
estCost(e) {
if (e is primitive)
total =total+cost(e)
else if (e=e1->e2)
total=total+estCost (e1)p1+estCost (e2)
else if (e=e1|e2)
total=total+estCost (e1) +estCost (e2)
}