## Slide 1: Paper Summary
Steven Lai

## Slide 2: Greedy Routing with Guaranteed Delivery Using Ricci Flow
Greedy routing
  Assign coordinates to nodes
  Message moves to neighbor closest to destination
  Simple, compact, scalable

## Slide 3: Problem: Greedy routing may get stuck
Can get stuck

## Slide 4: Solution: Use Ricci flow to make all holes circular
Greedy routing does not get stuck at holes.

## Slide 5: Ricci Flow in Sensor Networks
Build a triangulation from network graph
With node location: patch together the “local” Delaunay triangulations
Without locations: use landmark-based combinatorial Delaunay graph

## Slide 6: Ricci Flow in Sensor Networks
All edge length = 1 initially
  Introduces curvature in the surface
Use Ricci flow to reach target curvature k’
  Take tangent circle packing metric: γ=1/2, φ=0 initially
  Interior nodes: target curvature = 0
  Nodes on boundary C: target curvature = - 2π/|C|
  Modify ui = logγi by δ (κ’-κ)
  Until the curvature difference < ε

## Slide 7: Results

## Slide 8: Distributed localization of networked cameras
Place wireless cameras around an environment
Need to know locations
Costly to measure locations

## Slide 9: Distributed Localization of Cameras
If camera 1 sees person, then camera 2 sees person, learn about relative positions of cameras
As person moves around, estimate positions of all cameras

## Slide 10: Tracking with Kalman Filter: Estimation

## Slide 11: Camera Localization: Estimation

## Slide 12: Results: Model Complexity vs. Accuracy