## Slide 1: Planning for Improving Throughput in Autonomous Intersection Management
Tsz-Chiu Au
Department of Computer Science
University of Texas at Austin
Department of Computer Science
The University of Texas at Austin

## Slide 2: What can we learn from this video?
Notes: Indian traffic, no traffic signals, no stop sign, all vehicles just pass through directly.
What is amazing is that vehicles can still manage to pass through the intersection safely.
But in reality – many traffic accidents.
But still there are somethings we can learn from this traffic

## Slide 3: A Possible Solution to Traffic Congestion!
Notes: Explain what is buffer. New video with buffer shown.
emphasize the *difference* from India video
- no accidents
- also, all the cars communicate with a reservation manager
- use video from new simulator and show buffers

## Slide 4: Autonomous Intersection
Fully autonomous vehicles are technologically feasible with current technology
  the 2007 DARPA Urban Challenge
  for sale within 5-20 years
But today’s transportation infrastructure are designed for human drivers only
  Fail to utilize the full capacity of autonomous driving systems.
Autonomous Intersection Management (AIM)
  proposed by Dresner and Stone (2008)
  much more efficient than stop signs and traffic lights
Our goals:
  Realistically evaluate the protocol with real autonomous vehicles
  Improve the efficiency of the protocol.

## Slide 5: Outline
An introduction to AIM
A platform for evaluating the AIM protocol using real autonomous vehicles.
Identify factors that affect the efficiency of AIM
Methods for improving the throughput of AIM.
Notes: Need related work

## Slide 6
aim
autonomous intersection management

## Slide 7: The Reservation Idea
Vehicles call ahead to reserve a region of space-time on its trajectory in the intersection.
The intersection manager approves
or denies it.
Vehicles cannot enter intersection
without reservation.
The autonomous vehicle said:
The intersection manager said:
I’m arriving at time t at velocity v and turns left.
Sounds good to me!
Kurt Dresner and Peter Stone. A Multiagent Approach to Autonomous Intersection Management. JAIR 2008.

## Slide 8: Intersection Manager
Grid-based collision detection
First Come, First Served (FCFS)
Time 1
Time 2
Time 3
Time 4

## Slide 9: Intersection Manager
Approve the request only if the trajectory does not hit the trajectories of other vehicles.
Accept
Reject

## Slide 10: FCFS vs. Stop Signs and Traffic Light
Traffic level: number of vehicles per second per lane
Average delay: increased travel time due to intersection and traffic

## Slide 11: Is the protocol safe?

## Slide 12: Safety Measures
If all autonomous vehicles follow the protocol,
  Guarantee no collision.
Safety measures
  No crash even if some messages were dropped.
    A vehicle won’t enter an intersection if some messages are missing.
  When a crash occurs, sends STOP messages to all vehicles nearby.
    Avoid most collisions. But some are unavoidable.
Otherwise, collisions may occur.
  The situation is just like running the red light today.
  But we believe autonomous drivers can be made more reliable than human drivers.
STOP

## Slide 13: Sharing the Road with Human Drivers
Autonomous vehicles won’t displace manual-controlled vehicles in one day.
  There is a long transition period.
Some people enjoy driving.
Autonomous vehicles and manual-controlled vehicles will share some, if not all, of the roads in the future.

## Slide 14: The FCFS-Light Policy
Dresner and Stone, Human-Usable and Emergency Vehicle—Aware Control Policies for Autonomous Intersection Management, ATT 2006
FCFS-Light = Traffic light + FCFS

## Slide 15: Gradual Adoption of AIM

## Slide 16: Outline
An introduction to AIM
A platform for evaluating the AIM protocol using real autonomous vehicles.
Identify factors that affect the efficiency of AIM
Methods for improving the throughput of AIM.
Notes: Need related work

## Slide 17: Marvin – Our Autonomous Vehicle

## Slide 18: Mixed Reality Platform
Completely testing AIM on real hardware requires a fleet of autonomous vehicles
  Expensive and dangerous!
We implemented a mixed reality platform
  Testing a single (real) autonomous vehicle that interacts with many virtual (or simulated) vehicles.
Marvin – our autonomous vehicle

## Slide 19: Mixed Reality Simulation Platform
Step 1: establish UDP network connection
Step 2: create the proxy vehicle
Proxy vehicle

## Slide 20: Mixed Reality Simulation Platform
Step 3: constantly update the location, the direction, and the speed of the proxy vehicle
Proxy vehicle

## Slide 21: Mixed Reality Simulation Platform
Step 4: sensing information collected by the proxy vehicle are forwarded to the real vehicle
Proxy vehicle

## Slide 22: Mixed Reality Simulation Platform
Step 5: The real vehicle interacts with the intersection manager via the proxy vehicle
Proxy vehicle

## Slide 23: Mixed Reality Platform
AIM Messages
(Request, Confirm, etc.)
Physical State of the Vehicle
(GPS Location, Heading, Velocity, etc.)
Sensing Information
(Distance to the virtual vehicle in front, etc.)
Proxy vehicle

## Slide 24: Experiment Setup at a T-junction

## Slide 25: Mixed Reality in Action
Notes: - the first part is just a demonstration of the car working at the Urban challenge with other real cars on the road, using a conventional stop sign.
- So note that a lot of time is wasted while each of the cars wait for each other.
Go to our web page to download the video.

## Slide 26: Outline
An introduction to AIM
A platform for evaluating the AIM protocol using real autonomous vehicles.
Identify factors that affect the efficiency of AIM
Methods for improving the throughput of AIM.
Notes: Need related work

## Slide 27: What we learned from the reality check?
Identified areas in which previous simulations failed to capture the real-world performance of our autonomous vehicle
  Sensing and control errors are much higher
  Acceleration is slower
  Maximum speed is lower
To safely traverse the intersection, Marvin needs
  A larger buffer size
  Lower acceleration and maximum speed
Notes: Our previous simulations overly optimistic.

## Slide 28: Simulation Parameters
Static buffer size
Time buffer size
Model the performance on the vehicle
Errors in the movement of the vehicle
Time 1
Time 2
Time 3
Time 4
Maximum acceleration
Maximum speed

## Slide 29: The Effect of Increasing Static Buffer Size

## Slide 30: Using Realistic Simulation Parameters
In summary, the use of realistic simulation parameters decrease the performance of the protocol greatly.
Need to find ways to account for the larger buffer sizes and poorer vehicle’s performance.

## Slide 31: Outline
An introduction to AIM
A platform for evaluating the AIM protocol using real autonomous vehicles.
Identify factors that affect the efficiency of AIM
Methods for improving the throughput of AIM.
Notes: Need related work

## Slide 32: Traffic Congestion
Traffic congestion can still occur even in AIM.
Every intersection control mechanism has a maximum throughput
  If traffic level > maximum throughput, traffic congestion occurs
How can we increase the maximum throughput of FCFS?

## Slide 33: Little’s Law: N = λ T
N is the average number of vehicles inside the intersection
T is the average time a vehicle spends in the intersection
λ is the average arrival (entrance) rate of the vehicles at the intersection
  λ is also the throughput of the intersection

## Slide 34: Maximum Throughput
The maximum throughput an intersection can sustain is the maximum of λ
The maximum of N = maximum number of vehicles coexist in the intersection.
The minimum of T = minimum average time a vehicles spend in the intersection

## Slide 35: Increasing the Maximum Throughput
To increase the maximum throughput:
  increase the maximum of N
  decrease the minimum of T
It is hard to increase the maximum of N
  area of intersection / min. size of vehicles
  can’t push too many vehicles into the intersection at the same time
But there is a lot of room for reducing the minimum of T.
  by increasing the speed of the vehicles, vehicles will spend less time in the intersection
  The theoretical limit is the speed of light.

## Slide 36: To Reduce Traversal Time…
The speed of a vehicle depends on:
  The initial velocity when the vehicle enters the intersection.
  The acceleration in the intersection.
To reduce traversal time…
  Increase the arrival velocity
  Increase the acceleration
Two predictions:
  Preventing vehicles from stopping before entering an intersection can increase the throughput.
  Increasing the acceleration can increase the throughput.

## Slide 37: How to Prevent Stopping Before Intersection
Method 1: Obtain an accurate estimation of the arrival time and arrival velocity.
  Poor estimation → unable to reach the intersection at the arrival time and the arrival velocity → cancel the reservation at the last moment before entering the intersection → stop before intersection
I‘m late and/or unable to get up to speed
You should have cancelled the reservation earlier.

## Slide 38: How to Prevent Stopping Before Intersection
Method 2: Cancel reservation if the vehicle knows that it can’t arrive at the intersection at the given time and the given velocity.
  Early cancellation→ can submit a new request as soon as possible
  Early cancellation→ free up space-time tiles in the intersections
No, I can’t
Can you arrive at time tend and at velocity vend?

## Slide 39: Method 1: Better Estimation of Arrival Time and Arrival Velocity
Make sure that the proposed arrival time and velocity is achievable.
  i.e., there exists a sequence of control signals such that the vehicle, if follows the control signals correctly, will reach the intersection at the arrival time and velocity.
Formulate the estimation task as a multi-objective optimization problem:
  Among all possible sequences of control signals, find one such that
    the arrival velocity vend is the highest, and
    the arrival time tend is the smallest.
I’m confident I can arrive at time t and at velocity v

## Slide 40: The Sequence of Control Signals
For velocity-based controllers
  velocity schedule v(·) - the velocity of the vehicle at any time in [t1, tend]
For acceleration-based controllers
  acceleration schedule a(·) - the acceleration of the vehicle at any time in [t1, tend]
If a(·) is a piece-wise linear function,
  a(·) = <(t1,a1), (t2,a2), … , (tend,aend)>
At time t1, set
accel. to a1
At time t2, set
accel. to a2
At time t3, set
accel. to a3
At time tend, set
accel. to aend

## Slide 41: The Optimization Problem
Given
  The current time t1 and the current velocity v1
  The distance D between the current position and the intersection
  The speed limit of the road vmax
  The speed limit of the trajectory at the intersection vendmax
  The maximum acceleration amax and the minimum acceleration amin
Find a velocity schedule v(·) or an acceleration schedule a(·) such that vend is maximized while tend is minimized
At time t1, the velocity is v1
At time tend, the velocity is vend
D
SPEED
LIMIT
vmax
SPEED
LIMIT
vendmax
My max. accel. is amax
My max. decel. is amin

## Slide 42: The Time-Velocity Diagram
The function in the diagram is a velocity schedule v(·)
The visualization of constraints:
  The velocity cannot exceed the speed of the road vmax or be negative at any time.
  The arrival velocity vend cannot exceed the speed limit at the trajectory vendmax.
  The acceleration at any point in time must be within the limitations [amin, amax].
  The travel distance is D.
v(t)
Velocity
Time
vmax
v1
0
t1
tend
D
amin ≤ slope ≤ amax
vend < vendmax

## Slide 43: Optimal Velocity Schedule when v1 ≤ vendmax
Velocity
Time
vmax
v1
0
t1
tend
vendmax
Velocity
Time
vmax
v1
0
t1
tend
vendmax
Velocity
Time
vmax
v1
0
t1
tend
vendmax
Velocity
Time
vmax
v1
0
t1
tend
vendmax
Case 1:
D > Area1 + Area2
vend = vendmax
Case 2:
Area1 + Area2 ≥ D > Area3
vend = vendmax
Case 3:
D = Area3
vend = vendmax
Case 4:
Area3 > D ≥ 0
vend < vendmax
Area1
Area2
Area3
Always have a solution
When D ≥ Area3 , always arrive at the intersection at the maximum arrival speed vendmax in the smallest amount of time
When D < Area3 , arrive at the intersection at the highest velocity (< vendmax) in the smallest amount of time

## Slide 44
Velocity
Time
vmax
v1
0
t1
tend
vendmax
Velocity
Time
vmax
v1
0
t1
tend
vendmax
Velocity
Time
vmax
v1
0
t1
tend
vendmax
Case 1:
D > Area1 + Area2
vend = vendmax
Case 2:
Area1 + Area2 ≥ D > Area3
vend = vendmax
Case 3:
D = Area3
vend = vendmax
Case 4:
Area3 > D ≥ 0
No solution
Area1
Area2
Area3
No solution when D < Area3, because the vehicle is close to the intersection---can’t decelerate enough to a velocity below vendmax
When D ≥ Area3 , always arrive at the intersection at the maximum arrival speed vendmax in the smallest amount of time
Velocity
Time
vmax
v1
0
t1
tend
vendmax
Optimal Velocity Schedule when v1 > vendmax

## Slide 45: Guarantee arriving at the right time and at the right speed
The algorithm returns the optimal arrival time tend and optimal arrival velocity vend together with the velocity schedule (or acceleration schedule)
  avoid cancellation of reservation → avoid stopping before intersection
I will be on time and at the right speed
Then I expect no cancellation

## Slide 46: Method 2: Early Cancellation
Method 2: Cancel reservation if the vehicle knows that it can’t arrrive at the intersection at the given time and the given velocity.
  Early cancellation→ can submit a new request as soon as possible
  Early cancellation→ free up space-time tiles in the intersections
No, I can’t
Can you arrive at time tend and at velocity vend?

## Slide 47: The Validation Problem
Given
  The current time t1 and the current velocity v1
  The arrival time tend and the arrival velocity vend (assume vend ≤vendmax)
  The distance D between the current position and the intersection
  The speed limit of the road vmax
  The maximum acceleration amax and the minimum acceleration amin
Check whether a velocity schedule v(·) or an acceleration schedule a(·) exists such that the vehicle can arrives at the intersection at the given tend and the given velocity vend
At time t1, the velocity is v1
At time tend, the velocity is vend
D
SPEED
LIMIT
vmax
SPEED
LIMIT
vendmax
My max. accel. is amax
My max. decel. is amin

## Slide 48: The Time-Velocity Diagram
The visualization of the constraints:
  v(t1) = v1 and v(tend) = vend
  The velocity cannot exceed the speed of the road vmax or be negative at any time
  The arrival velocity vend cannot exceed the speed limit of the trajectory vendmax
  The acceleration at any point in time must be within the limitations [amin, amax]
  The travel distance is D
v(t)
Velocity
Time
vmax
v1
0
t1
tend
D
amin ≤ slope ≤ amax
vend < vendmax

## Slide 49: The Liquid Metaphor
v(t)
Velocity
Time
vmax
v1
0
t1
tend
D
slope = amin
vend < vendmax
Satisfied all constraints except the travel distance constraint D
slope = amax

## Slide 50: The Liquid Metaphor
Velocity
Time
vmax
v1
0
t1
tend
slope = amin
vend < vendmax
Satisfied all constraints except the travel distance constraint D
slope = amax
Area3
Area2
Area1
AreaL
AreaR

## Slide 51: Feasible and Infeasible Cases
Infeasible cases
  Case 4: D < AreaL + AreaR
  Case 5: AreaL + AreaR + Area1 + Area2 + Area3 < D
Case 1:
Case 2:
Case 3:

## Slide 52
The algorithm returns true if and only if an acceleration schedule exists for arriving at the intersection at the given time and the given velocity.
  In the infeasible cases, cancel the reservation as early as possible
  In the feasible cases, the acceleration schedule can be used to control the vehicle.
No, I can’t
Can you arrive at time tend and at velocity vend?
Guarantee Early Cancellation of Reservations

## Slide 53: Planning-Based Controllers vs. Heuristic-Based Controllers
Planning-Based
Controller
Heuristic-Based
Controller
Conducted an experiment to compare with the previous vehicle controller.

## Slide 54: AIM vs. Signs and Traffic Signals
With the help of the motion planning algorithms, AIM is still better than stop signs and traffic signals when realistic simulation parameters are being used.

## Slide 55: Increasing Throughput by Increasing Acceleration
Increasing acceleration can reduce the traversal time of the vehicles.
  especially when many vehicles have stopped before the intersection
An increase of acceleration can increase the throughput
  Acceleration↑ → Speed ↑ → Time (T) ↓ → Throughput (λ)↑
Intuitively, the trajectory of fast moving vehicles reserves less tiles in the reservation grid
  The intersection can handle more trajectories.

## Slide 56: Acceleration vs. Throughput
The throughput (λ) is approximately proportional to the square root of the acceleration (a).
a
λ
Traffic level = 0.16 vehicles / second / lane
a

## Slide 57: Conclusions
The mixed reality platform.
Realistic simulation parameters.
Analysis of the relationship between the maximum throughput and the vehicle’s performance.
Motion planning algorithms.
Notes:   Realistically evaluated the AIM protocol.
  Little’s Law: Prevent stopping before intersections and increase acceleration.
  Motion planning techniques to prevent stopping before intersections.
  Conducted experiments to evaluate the planning-based controllers and the acceleration.

## Slide 58: Future Work
Implement the motion planning algorithms on Marvin.
Optimization of reservations
Network of Intersections
Partially autonomous vehicles
  Adaptive cruise control
  Autonomous parallel parking
  Traffic sign recognition
  Lane departure warning systems

## Slide 59: My Other Work
Non-zero-sum, repeated games
  How to cope with errors in the intersection among agents
  Learning from intersection traces
AI planning
  HTN planning
  Planning with violate, external information
Case-based reasoning
  Reuse of previous problem solving experience
  Derivational analogy
Iterated Prisoner’s Dilemma
Opponent
Agent1
Agent2
Agent3
Interaction
Traces

## Slide 60
Thank you!
Any Questions?